## Slide 1: Embedded Systems

## Slide 2: Basic Components of Computer
CPU
Memory
I/O
CPU
Memory
I/O
Motherboard

## Slide 3: Microcontrollers
CPU
ROM RAM
I/O
A single chip (SoC)
Subsystems:
Timers, Counters, Analog
Interfaces, I/O interfaces
Memory

## Slide 4: LPC 1768

## Slide 5: Microprocessor vs Microcontroller

## Slide 6: Microcontrollers

## Slide 7: Embedded System General Block Diagram
Microcontroller
(uC)
sensor
sensor
sensor
Sensor conditioning
Output interfaces
actuator
indicator

## Slide 8: Embedded systems overview
Embedded computing systems
  Computing systems embedded within electronic devices
  Nearly any computing system other than a desktop computer
  Billions of units produced yearly, versus millions of desktop units
Lots more of these, though they cost a lot less each.

## Slide 9: Some common characteristics of embedded systems
Single-functioned
  Executes a single program, repeatedly
Tightly-constrained
  Low cost, low power, small, fast, etc.
Reactive and real-time
  Continually reacts to changes in the system’s environment
  Must compute certain results in real-time without delay

## Slide 10: An embedded system example -- a digital camera
Single-functioned -- always a digital camera
Tightly-constrained -- Low cost, low power, small, fast
Reactive and real-time -- only to a small extent
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD

## Slide 11: RISC vs CISC
RISC – Reduced Instruction Set Computer
CISC – Complex Instruction Set Computer
2. RISC processors have a fixed instruction size. In a CISC microprocessors such as the x86, instructions can be 1, 2, 3, or even 5 bytes. For example, look at the following instructions in the x86:
1. One of the major characteristics of RISC architecture is a large number of registers. All RISC architectures have at least 8 or 16 registers. Of these 16 registers, only a few are assigned to a dedicated function. One advantage of a large number of registers is that it avoids the need for a large stack to store parameters.

## Slide 12: RISC vs CISC
3. RISC processors have a small instruction set. RISC processors have only basic instructions such as ADD, SUB, MUL, LOAD, STORE, AND, OR, EOR, CALL, JUMP, and so on.
The limited number of instructions is one of the criticisms leveled at the RISC processor because it makes the job of Assembly language programmers much more tedious and difficult compared to CISC Assembly language programming.
This is one reason that RISC is used more commonly in high-level language environments such as the C programming language rather than Assembly language environments.

## Slide 13: RISC vs CISC
4. The most important characteristic of the RISC processor is that more than 99% of instructions are executed with only one clock cycle, in contrast to CISC instructions.
5. RISC processors have separate buses for data and code.

## Slide 14: Microcontroller Architectures
CPU
Program + Data
Address Bus
Data Bus
Memory
Von Neumann
Architecture
CPU
Program
Address Bus
Data Bus
Harvard
Architecture
Memory
Data
Address Bus
Fetch Bus
0
0
0
2n

## Slide 15: RISC vs CISC
6. Because CISC has such a large number of instructions, each with so many different addressing modes, microinstructions (microcode) are used to implement them.
RISC instructions, however, due to the small set of instructions, are implemented using the hardwire method.
7. RISC uses load/ store architecture. In CISC microprocessors, data can be manipulated while it is still in memory.
8. Memory Mapped IO in RISC and IO mapped IO in CISC

## Slide 16: RISC vs CISC